Architecture of NRF24L01+ in RS module project

Gateway is the main module who is in command (Master)
Nodes are modules can either send data or act on data (Slave) – SENSOR - ACTUATOR

Init:
- SPI needs to be initialized
- NRF chip needs to be initialized
- “Network” needs to be initialized

# Network init
- Master SCAN
  - Scan entire RF band for optimal reception
  - Select RF freq
  - In case multiple masters, every master has most likely a different RF freq.
- Slave BOOT
  - Power up and request over full band Request based in UID (96bit=12byte)
  - If no signal within 10ms go to next
  - If response ACK, then continue PAIRING
- Master/Slave PAIRING
  - Master will send Slave module address (MA)
  - Slave will store Address in RAM
  - Slave will respond to Master Module Adress will now be used
- Slave SENSOR:
  - MASTER will send TDMA command INTERVAL (Time Division Multiple Access)
  - MASTER will send TDMA command START
  - Slave will send first time its data and goes in sleep
  - Slave will wakeup after INTERVAL
  - Slave will send data
  - Slave will listen for 1 second for new commands
    - NO_ACTION
    - RESET
    - INTERVAL
    - GIVE ADDITIONAL DATA like Vbat, Uptime, UID,….
- Slave ACTUATOR
  - Does not go in standby/sleep
  - Always listing

# NRF setup
The nRF24L01 supports only 6 data pipes (addressable communication channels) for simultaneous communication. Shared Address with Unique Payload Identification

Configure all transmitters to use the same address but include a unique identifier in the payload.
Data pipe 0 (RX_ADDR_P0)
NRF24L01_EN_RXADDR_DEFAULT_VAL = 0x03

Set for 3 bytes (not 4 or 5, is not needed)

## Enhanced Shockburst
Preamble	Address Channel	PCF	Payload	CRC

Preamble :	10101010 or 01010101
Address Channel:	0x03 (See above)
PCF:	Packet Control Field (9bit)
Payload length (6 bit) → used if the Dynamic Payload Length function is enabled.
PID (Packet identification) (2 bit)
No Acknowledgment flag ( NO_ACK ) (1bit)
Payload:	0 to 32 bytes (see below)
CRC

## Payload
The payload will be filled with a kind of MODBUS protocol.
Without the CRC because this is captured by the NRF.
Without the additional TDMA option, so that reading data not only can be done sequentially master slave approuch
### Summary
- Minimum Modbus RTU message length: 4 bytes.
- Typical request length for reading/writing: 8–29 bytes, depending on the operation and data points.

Request
Slave / Adress 1byte	Function code / 1byte	Start Address (2 bytes)	Quantity (2 bytes)

Response
Slave / Adress 1byte	Function code / 1byte	Byte Count: / 1 byte (number of data bytes)	Data (N bytes)

### Slave Address
Range: 1 to 247.
- 1 to 247: Usable addresses for slave devices.
- 0: Reserved for broadcast messages (no response from slaves).
- 248 to 255: Reserved and typically not used in standard implementations.

### Function code
Depending on the FC, the data field can be different
We use the following FC:
1	=	Read Coils 1bit
5	=	Write Coil 1 bit
4	=	Read Register 16bit
6	=	Write Register 16 bit
8	=	Diagnostics
43	=	Read Device Identification

### Read Coils or Registers (Function Codes 01, 02, 03, 04)
#### Request
#### Address (1 byte) + Function Code (1 byte) + Start Address (2 bytes) + Quantity (2 bytes)
#### Response
#### Address (1 byte) + Function Code (1 byte) + Byte Count (1 byte) + Data (N bytes)

TDMA Response, same format as normal response
Example for a Temp/Humid sensor this could be:
Address + FC4 + 0x04 + TempMSB+TempLSB+HumidMSB+HumidLSB

### Write Single Register or Coil (Function Codes 05, 06)
Request and Response:
### Address (1 byte) + Function Code (1 byte) + Register/Coil Address (2 bytes) + Value (2 bytes)